Minimize or exit SPRING.

## 2.10 Add Projection, Reproject, Load into GIS

SPRING does not add the projection to the shapefile so you will need to add it using ArcCatalog. Remember it is UTM Zone 14, WGS84, in this case. You may need to then reproject to UTM Zone 14, GRS80. Then use the shapefile as is or convert it to a personal geodatabase and load it into and work with it in your favorite GIS.

# 3.0 SPRING Export/Import

There may be a need to export a segmentation from SPRING to use in a GPS data logger for field data collection. The following details how to export a segmentation to a shapefile.
## 3.10 Export segementation from SPRING as TIF

In the Control Panel popup, highlight the Infolayer that represents the segmentation to export, then select File | Export. In the Export popup, leave Format: set to TIFF/GeoTIFF. The Mono radio button should be selected. Click the Save… button.

Another popup should appear that will allow you to navigate to an appropriate directory where the tif can be exported. Click on the Save button.

## 3.20 Convert TIF to GRID

Start an ArcMap session and load in the TIF file. When the TIF loads it will be black. Highlight and right click the TIF filename in the table of contents. Highlight Data, then Export Data. The Export Raster Data popup should appear. Navigate to the appropriate directory Location:, use the default filename and confirm the output Format: is GRID. Click on Save. When prompted to add the exported data to the map as a layer, click on Yes. Right click and remove the TIF file from the table of contents.

  1. Convert GRID to Shapefile
With the GRID file loaded into ArcMap, use the Raster to Polygon tool in ArcToolbax to convert the GRID to a shapefile. Make sure that the Simplify polygons checkbox is not checked! The shapefile will automatically be added to ArcMap.

At this point, an attribute or label field can be added to the shapefile and random or other types of subsets of the segments can be made. Another shapefile can be created from the subset selection.

Exit Arcmap.

  1. Convert Shapefile to ASCII SPRING

To import the subset selection, start SPRING. Select FILE| Convert to ASCII SPRING…. A Conversion ASCII SPRING popup should appear. Click on File: and Navigate to the directory where the shapefile is located, highlight it, and click on Open. Make sure that SPRING Model: is set to Thematic. In the Attributes window of the Conversion ASCII SPRING popup, highlight the field that contains the attributes or labels. Near the bottom of the popup, in the ASCII File Name: window, type in a meaningful filename (e.g., sps3xsel), then click on Apply. The software will run and the Conversion ASCII SPRING popup will close by itself. The software will have created two ascii files, one with the ASCII File Name: supplied with _L2D.spr concatenated (e.g. sps3xsel_L2D.spr) and another with the ASCII File Name: supplied with _LAB.spr concatenated (e.g. sps3xsel_LAB.spr).

  1. Import ASCII SPRING to SPRING Infolayer

Select File| Import, click on the Directory… button and navigate to where the _L2D.spr and _LAB.spr files are located. The ASCII-SPRING files should appear in the window just below Format: which should be set to ASCII-SPRING. Highlight the file with the _L2D.spr ending,

set Entity: to Lines with topology (which is another way of saying polygons), then make sure Category… is set to a thematic one, in PI: type an appropriate filename (e.g. sps3xsel) and then click on Execute.

The new PI should appear in the thematic Category in the Control Panel. In the Import popup, select the file with the _LAB.spr ending. Set Entity: to Labels, and leave everything else the same, including the PI: and click on Execute. Something like the following Notice should appear. Click on OK. In this case, the imported classes already existed inside of SPRING.

Close the Import popup. Click on Draw and rezoom to you imagery. With the newly created PI highlighted, select the Lines and/or Classes checkboxes and then Draw to confirm that the data has been imported.

At this point, an image classification can be started and this newly imported thematic PI can be imported into the Training popup.